## Slide 1: Detection of failures
Doug Curry
USPAS, January 2017

## Slide 2: Machine Modes – segmenting the machine
LINAC
CCL Beam Stop
Front-End:
MEBT Beam Stop
LINAC
Front-End
Accumulator Ring
Injection Dump
LINAC Dump
RTBT
Extraction Dump
Target
MEBT Beam Stop
CCL Beam Stop
L-Dump
I-Dump
E-Dump
Target
  **all systems have to be made up
Beam operations can occur in areas that are ready to accept beam
Downstream devices of beam destination are ignored

## Slide 3: Protection methods
Fast Protection (micro-seconds)
  Custom Hardware
    Discrete logic, FPGAs, Operational Amplifiers, comparators
    RF, pulsed magnets, BLM, BCM, …
Slow Protection (milli-seconds)
  PLC
    Gate valves, current transformers, water flow, …
Soft Protection (seconds)
  Software
    Magnet settings (~450 magnets at SNS), BLM voltage (Ion Chamber), …
  Alarms
    Human interaction, on the order of several seconds

## Slide 4: Is the machine location ready for beam?
Wire scanner
gate valves
stripper stripper foil
target
Beam Dumps
Extraction Septum
Limit switches

## Slide 5: Water Leaks
Outer Reflector Plug
Inner Reflector Plug
Water
Slow
Interlock

## Slide 6: Target Monolith

## Slide 7: Failure identified…what now?
H2 supply
Vacuum
H2 return
Core Vessel helium
Loop 3 light water flow
Vacuum
Fillet weld sealing water annulus
Helium annulus termination
Pipe inside of a pipe inside of a pipe…
Shielding
High radiation area

## Slide 8: What now?
The hydrogen transfer lines and associated vacuum envelopes are Passive Credited Engineered Controls in the Accelerator Safety Envelope
  Filling the helium annulus with water changes the pressure conditions on the outer vacuum jacket, which requires analysis for possible remediation scenarios
Operating the core vessel with a humid atmosphere must be assessed for conditions such as galvanic action, corrosion, and so on
Water break off from transfer line
Water annulus termination weld to helium line
Top Downstream transfer and water lines
Helium annulus termination, water flowing from this location

## Slide 9: Water leaks
MEBT Chopper Target Failure
  Internal beamline component
  Complete disassembly of the MEBT
  DTL GV was closed
  No direct interlock
    Vacuum??
MEBT
Chopper
Target
MEBT Chopper
MEBT

## Slide 10: SNS Injection Region
Direct H- and H0 waste beams to IDmp beam line
Merge H- and circulating P beams
Where does the beam go without primary stripper foil?
H- beam from Linac
Thin “Primary” Stripping Foil
To Injection
Dump
Thick Secondary Foil
H-
Dipole magnets
H0
p
150 kW capacity

## Slide 11: Beam Current Monitors (BCMs)
Nano Coulomb Detector (NCD)
100 kW Dump
  Conservative
Example of a fast interlock
  FPGA based
Large dynamic range
Torn stripper foil
NCD
Extraction dump

## Slide 12: NCD (Nano Coulomb Detector)
A stripline design is optimized for beam response for a particular harmonic
Measuring capability
  120 dB dynamic range
  nA to several Amps
Stripline BPM
nA
1mA
Post mortem
waveform capture
Integrated power is verified against MPS threshold settings
Calibration tables
4 electrodes
C. Deibele

## Slide 13: Beam Current Analysis
Ideal
Gaussian
For n, is constant
(assuming that the charge is constant)
I(t)
t
T
t
T
I(t)
Fourier Series
Periodic Function
C. Deibele

## Slide 14: Infinite pulse train of current (constant charge)
Harmonic Number n
Comparison of relative magnitude between and versus
C. Deibele

## Slide 15: Observations of Series Analysis
Results of study
n=0 is unaffected, n=1 changes only by ~2% when σ varies from
10 psec to 100 psec.
It can not be expected to transport this wild range of in the linac!
Assume FWHM varies by ~5%.
use the n=1 term, baseband emi can be filtered. can be considered constant for 5% variation of FWHM.
But, what is the detector?? It needs to be capable of a measurement
which is independent of beam position and is unaffected by emi.
C. Deibele

## Slide 16: NCD Design
Desire output to be independent of and
Single Shorted Electrode
4 feed thrus give1% intensity variation on beam position over 95% of beampipe – HFSS simulation
Signal is combined using phase matched cables
Output= A+B+C+D
S. McTeer / K. Gawne
Nanocoulomb Detector
Has implications
A
B
D
Assume I(t) has positional dependence w.r.t. time
Not described in this talk
C
C. Deibele

## Slide 17: NCD Design
A
C
B
D
NCD was mapped using a NWA and
taught wire to simulate beam. The signal
error had a current measurement
(independent of position) in the beampipe with
a standard deviation of 1.3%
Total expected theoretical error is therefore
2.43% (connector/hybrid + bunch length).
C. Deibele

## Slide 18: Schematic of Analog Hardware
Output of each section is logarithmically proportional
to beam current. Log-amps measure rf-power.
Calibration!
Each channel requires nonlinear signal processing to
merge the multiple channels into one.
Described next slide
Not described in this talk
Not described in this talk
C. Deibele

## Slide 19: How a Log Amp operates
Output signal is proportional to the input power
Output is down-converted to baseband
Noise from nearby sources (Kickers, Magnet Supplies, etc.) is filtered out before the log-amp and does not affect measurement
Has an intrinsic rise-time
C. Deibele

## Slide 20: First Measurements
Reflections caused by head of beam minipulse
and the length of the cable round trip travel time.
C. Deibele

## Slide 21: Schematic of Analog Hardware
Added circulator and single stub tuner for reflection
C. Deibele

## Slide 22: After circulator and stub
Gaps are progressively getting smaller w.r.t. time purposely
Not all gaps are identical due to source issues
Note:
C. Deibele

## Slide 23: Photograph of installation
NCD
Combiner+Circulator+Stub
C. Deibele

## Slide 24: Differential BCM
Measure losses in the Linac
Example of a fast interlock
Beam loss

## Slide 25: BLMs
Used at all facilities
Neutron detectors PMT/scintillator (DTL/CCL)
Ion Chamber (SCL → Target), argon filled
At SNS linac beam stops 20 – 30 us after BLM trip
  If trip occurs upstream of or within the accumulator ring, can stop accumulation, but beam that has already accumulated will be sent to target – anywhere from small to full intensity
  If trip occurs downstream of ring, can only prevent the next pulse from beginning the accumulation process
Fast interlock < 30 us total, includes BLM response time
Can stop accumulation
before extraction
Prevent next pulse only

## Slide 26: Dissolved gas analyzer
High Voltage Converter Modulator (HVCM) produce the pulsed power needed to power the klystrons
DTL Modulator
  Impurities levels permitted arcing
  Acetylene build up
  Eventually sufficient quantities accumulated
  The gas ignited causing deformation of the tank. The ½ inch (12.7 mm) steel plate bowed about 3 inches (76.2 mm)
Soft interlock is sufficient
  Occurs over hours/days

## Slide 27: LEBT Beam in Gap measurements
CHuMPS (Chopper “und” MPS)
Fast amplifier with comparator circuit
Fast interlock
Time (ms)
Current (uA)
Ion source waveform
1 ms
no beam in gap
Series of gates from the timing system generate the beam in gap checks
+
−
Comp
V Ref
T Ref
C. Deibele

## Slide 28: Pulsed Magnets
SNS Injection Kickers
  Directly impacts the beam distribution on the target, too big, too small
  60 Hz operation, 5M repetitions per day, 1.27B repetitions over 8 months
  Waveform Monitors validate amplitude and timing
  Fast interlock

## Slide 29: Pulsed Magnets
SNS Extraction Kickers
Fast interlock
Extraction Energy | 1.0 GeV
Extraction Type | Single-turn
Flat-top length | > 700 ns
Extraction rate | 60 Hz
Rise time | 200 ns
Operating Voltage | -35 kV
Operating Current | -2.5 kA
Typically
~ 695 ns
E-Kickers
8-14
1.0 GeV
945 ns
1.3 GeV
911 ns
Ring Revolutionary period

## Slide 30: Pulsed Magnets
Misfiring Extraction Kickers
  Usually isolated to a single kicker
    Production periods run 13 of 14 Kickers
      Hot-read spare kicker is run out of time 5 microseconds
  Thyratron jitter and drift dominate failure modes
    High power electrical switch
    5.2 million cycles per day
  Power supply failure
  Timing reference
    Temporary PLL jitter at the Timing Master
    Results in all 14 misfiring “kick in the middle of the beam pulse
RTBT collimators are designed to intercept beams that are off-center due to extraction kicker mis-fires.
RTBT Collimator
Beam gap
~250 ns
SNS
Extraction
Kickers

## Slide 31: Magnets
Magnet readbacks
Example of a Soft interlock
  software interface with the MPS hardware
Example: SNS lock-down of RTBT quad and dipole corrector magnet currents
Trip limits set to +/-5% on quads and +/-0.5 A on dipole correctors

## Slide 32: Magnets
PLC limits reside local to the system(s)
  One system per destination change on large dipole magnets
    Linac, HEBT, Ring, Extraction and Target
    Current Transformers provide magnet setting levels
    Values are locked in after tuning
Linac
Dependent on machine mode settings
Slow interlock
Injection
Extraction
Target

## Slide 33: Magnets
Fast interlock

## Slide 34: Magnets
Fast interlock
  False reporting
  Can prohibit reliable beam transportation
“Noise” Trips
  Beam image currents
  Power supply switching noise
  Other miscellaneous sources
    RF, transformers, long parallel cable runs, etc…
Beam image current

## Slide 35: Insertable devices
Position indicators
Beam measurement
  Harps, wire scanners, faraday cups, etc..
Halo mitigation
  Scrapper postion
Isolating vacuum
  Gate valves
gate valves
Limit switches
Wire scanner

## Slide 36: Cavity damage caused by slow MPS response times
Continued degradation of RF gradients
  Eventually led to measuring MPS response times
Fast interlock ⇒ slow interlock
  20 us design, operating at 200 us, order of magnitude above specification
  Capacitors installed to mitigate false trips, additional charge sustained “good” operating condition for up to 300 us in some cases
Organizational Impacts
  Lack of confidence in system
    Degrading system performance…MPS problems again!!!!!
  Damaged Cryo-cavities
Beam Position Monitor
BLM fault
MPS permissive

## Slide 37: Cryo-cavity damage
RF in
Sub-link node
Main-link node
Beam Position Monitor
Sub-link
Main-link
Copper
link
Fiber
links
Top

## Slide 38: MPS failure
No reporting
Output enable stuck high
  Provides a false MPS status to the top level node and permits continued beam production
Firmware implementation did not match the architecture approved by the review committee
  Single clock source generated at the lowest node in the “chain”
  Each node simply grants or prevents the passing of the permissive signal
  Passed local clock source instead of original clock source
Introduced 2 failure points
Sub-link
Main-link
Copper
link
Fiber
links
Top
Local clock source
Gated clock input stuck at “1”
BLM
RF

## Slide 39: MPS IC failure
Caught by machine specialist
  Noted BLM faults with no associated system faults
  MPS and RF team performed independent tests and verified failure mode
Local clock source
single clock source
Faulted node
Stuck at 1
Fault detected
✅ False status passed
Depth of problem is dependent on the number of nodes in the chain and the location of the fault
  16 inputs per node multiplied by the number of nodes in the chain
Isolated to the individual node
  16 inputs max
Stuck at 1