## Slide 1: LLRF with direct sampling
Jesus A. Vasquez Stanescu
USPAS 2017 Low

## Slide 3: Description
Quarter Wave Resonator (QWR) cavities, with resonance frequencies of 80 MHz and 160 MHz
RF Controller can control 8 cavities
The RF signals picked- up from the cavities are sampled by RF ADCs
Control loop is implemented on a FPGA
The main perturbations are cause by microphonics [Hz to kHz] (pressure variations in helium, temperature, mechanical vibrations, change in cavity resonance by currents/charges).

## Slide 4: System block diagram
Measure reflected and forward powers
Adapt amplitude levels of RF signals

## Slide 5: Algorithm block diagram

## Slide 6: RF ADCs
ADS42JB69, 16 bit, 250 MSPS
Undersampling at 121.9 MHz
Noise is dominated by clock jitter
16 bit ADC SNRmax = 98dB
tjmin ~ 0.016 ps
10 bit -> 62dB -> ~1.04 ps

## Slide 8: System block diagram

## Slide 9: RF DACs
200 MHz signal
Direct Digital Synthetizer (FPGA) generates 40 MHz
Numerical Controlled Oscillator (DAC) generates 160MHz
DAC acts as Digital Up Converter mixing the 40MHz and 160MHz to produce the 200MHz

## Slide 10: Algorithm block diagram

## Slide 11: Non-IQ sampling
The sampling frequency is
  N samples in M IF periods
  Example M=3, N=25
  errors from DC offsets, clock jitter, ADC quantization, noise reduced
  but more latency due to sampling M IF periods