## Slide 1
Ram C. Dhuley
USPAS – Cryogenic Engineering
June 21 – July 2, 2021
Cryogenic Equipment – Part II
(content courtesy: Tom Peterson/SLAC)

## Slide 2: Outline
Cryogenic equipment
  Mechanical cold seals
  Pressure relief valves
Photo stories
  Feed box fabrication sequence
  LCLS II SRF cryomodule assembly

## Slide 3: Metallic cold seals
The Fermilab Tevatron includes about 1200 interconnects (magnet-to-magnet and magnet-to-endbox), each of which includes
  An insulating vacuum to beam vacuum seal
  A 4.0 K, 2 bar helium to vacuum seal (“single-phase seal”)
  A 4.0 K, 1.2 bar helium to vacuum seal (“two-phase seal”)
  An 80 K, 3 bar nitrogen to vacuum seal

## Slide 4: Metallic cold seals
Tevatron magnet interconnect (one side)
Nitrogen
2-phase He
Single-phase He
Beam tube
Other side of interconnect

## Slide 5: Metallic cold seals
    Fermilab-designed brass
    wedge clamp -- we like these brass wedge clamps at Fermilab
    Aluminum Helicoflex c-seal with internal inconel spring. Surface finish of flange is about 80 micro-inch (2 microns). Seal is designed specifically for this finish.
Seals for nitrogen and 2-phase helium lines

## Slide 6: Metallic cold seals
Stainless steel, elliptical “Conoseal” from Aeroquip Corp.
Silver coated 0.0005” (13 micron) thick plating. Coated locally.
Indium, copper, and gold plating each failed. (Indium creeps, gold had poor adhesion to the SS.)
Good success with silver, although if the silver corrodes, then it leaks.
Similar 4-bolt Fermilab-designed brass clamp on tapered flanges.
Seals for single-phase helium

## Slide 7: Metallic cold seals
Indium is popular but not universally endorsed for helium to vacuum metal joints
  Indium seals used successfully for SF to vacuum seals at Fermilab’s Magnet Test Facility
  Tevatron experience suggested creep and long-term failure
  Indium seals used extensively at Jlab for long-term seals (See paper by Benesch and Reece, Advances in Cryo Engineering, Vol. 39A, pg 597)
A very sensitive and successful leak test generally results in a leak tight SF seal. Such a leak check requires a local test fixture around the seal or double-seal.
“Cold leaks” (4.5 K) may be found which are likely just due to greater He density and leak rate cold.
Some concluding remarks

## Slide 8: Spring loaded relief valves
Spring loaded valves are routinely used to relief excessive
pressure in helium piping or on a helium bath

## Slide 9
The following photos illustrate the sequence of major steps in fabrication of a large cryogenic box in industry
A “distribution feed box” or DFBX for the inner triplet magnets in LHC
Eight boxes fabricated at Meyer Tool near Chicago and shipped to CERN
Photo story 1 - Fabrication of a magnet current “feed box”
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 10
Build from top plate, down
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 11
Hang helium vessel
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 12
Connect helium vessel
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 13
Prefabricated piping
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 14
Install prefabricated piping
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 15
Splice and package internal cables
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 16
Splice and package internal cables
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 17
Splice and package internal cables
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 18
Install remaining internal piping
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 19
Weld close helium vessel
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 20
Leak check helium vessel
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 21
Wrap with multilayer insulation (MLI)
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 22
Prefabricated thermal shields
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 23
Install thermal shields
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 24
Weld vacuum shell
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 25
Final leak check and inspection
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 26
Shock-absorbing shipping frame
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 27
Photo story 2 – Assembly of LCLS II SRF cryomodule (pictures from FNAL and Jlab)
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 28
Cavity string – Jlab cleanroom
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 29
Cavity string out of cleanroom (Fermilab)
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 30: Welding and leak checking cryogenic pipes
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 31: Attaching cavity string to cryogenic structure
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 32: Integration of cavity string with cryogenic pipes and supports
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 33: Assembly at alignment and instrumentation station
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 34: Thermal shield installed
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 35: Multilayer insulation wrapped
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 36: Assembly into vacuum vessel
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 37: Instrumentation wiring
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)

## Slide 38
Final cryomodule assembly
Ram C. Dhuley | USPAS Cryogenic Engineering (Jun 21 - Jul 2, 2021)